## Slide 1: Lec 6/7: Signaling Basics
Appendix A & Lesson 3
September 25 and 27, 2017

## Slide 2: Main Points for Lecture
Basic Concepts Of Electricity
Voltage and Current
  POTENTIAL ENERGY AND VOLTAGE
Components of a Circuit
Resistance
  Ohm’s Law
Capacitance

## Slide 3: Learning Objectives
Understand the relationship between voltage, potential energy and current.
Understand the principles of Ohm’s law
Understand the functions of resistance and capacitance in an electrical circuit.

## Slide 4: Why is this important?
Electrical properties of neurons can be described in terms of electrical circuits.
Helps us understand how a neuron behaves when current flows into it (ion channels open) or why unmyelinated neurons conduct more slowly than do heavily myelinated neurons

## Slide 5: Why is this important?
Biophysical properties of neurons are often difficult for students to fully grasp, making this topic particularly well-suited for first understanding basic electrical circuits and the relationships between current flow, voltage and resistance and capacitance elements.

## Slide 6: Hydraulic and electric circuits
A source of energy is required to keep the current flowing.
In hydraulics, the source is a pump
In electronics, it is a battery.

## Slide 7: Hydraulic and electric circuits
Neither water nor electrical charge is created nor lost within a closed circuit.
Water flow is similar at all points in the hydraulic circuit since no water is added or removed.
In the electrical circuit, current flow is similar within the closed loop.

## Slide 8: Components of electrical circuits

## Slide 9: Basic Concepts Of Electricity
Charge
  Concept of electricity arises from an observation of nature
  Observe a force between objects, that, like gravity, acts at a distance.
  The source of this force has been given the name charge.
  There are two types of electric charge.
    Opposite types of charge attract, and like types of charge repel.

## Slide 10: Basic Concepts Of Electricity
Conductors
Made of atoms whose outer electrons have relatively weak bonds to their nuclei
When a bunch of metal atoms are together, they gladly share their outer electrons with each other, creating a "swarm" of electrons not associated with a particular nucleus.
A very small electric force can make the electron swarm move. Copper, gold, silver, and aluminum are good conductors.
So is saltwater.
Insulators
Materials whose outer electrons are tightly bound to their nuclei.
Modest electric forces are not able to pull these electrons free.
When an electric force is applied, the electron clouds around the atom stretch and deform in response to the force, but the electrons do not depart.
Glass, plastic, stone, and air are insulators.

## Slide 11: The Basics: Elements, Atoms, and Ions
Atoms
Smallest quantity of an element that retains the properties of that element
Contain a nucleus
  Neutrons: neutral in charge
  Protons: carry a positive (+) charge
  Electrons: carry a negative (−) charge
    Electrons orbit the nucleus

## Slide 12: The Basics: Elements, Atoms, and Ions
Atoms
When an atom gives up an electron, it becomes positively charged
When an atom takes on an electron, it becomes negatively charged
Ion
  A charged atom

## Slide 14: Current
Flow of charge.
Charge flows in a current.
Reported as the number of charges per unit time passing through a boundary.
The SI unit for current is the ampere (A)
An ampere is one coulomb per second
The rate of flow of charge is current. An ampere is the flow of one coulomb through an area in one second.
http://cnx.org/contents/031da8d3-b525-429c-80cf-6c8ed997733a@9.94.

## Slide 15: Current
The direction of current flow is from positive to negative.
The direction of conventional current is the direction that positive charge would flow.
In ionic solutions, such as salt water, both positive and negative charges move.
  This is true in nerve cells.

## Slide 16: Current
(a) Positive charges move in the direction of the electric field and the same direction as conventional current.
(b) Negative charges move in the direction opposite to the electric field.
Conventional current is in the direction opposite to the movement of negative charge.
The flow of electrons is sometimes referred to as electronic flow.
http://cnx.org/contents/031da8d3-b525-429c-80cf-6c8ed997733a@9.94.

## Slide 18: Current
Current is carried by both positive and negative charges in saltwater:
If we put ordinary table salt in water, it becomes a good conductor.
Table salt is sodium chloride, NaCl.
The salt dissolves in water, into free-floating Na+ and Cl- ions.
Both ions respond to electric force and move through the saltwater solution, in opposite directions.

## Slide 19: What is the force?
Water (H20)
  Atoms held together by shared electrons
  Polar molecule
    Opposite charges at opposite ends
Chemical properties of water enable it to dissolve salt crystals into their component ions

## Slide 22: From current to voltage
Electrons can flow only when they have the opportunity to move in the space between the atoms of a material.
There can be electric current only where there exists a continuous path of conductive material providing a conduit for electrons to travel through.
E.g., water can flow through the tube if and only if the tube is open and there is no blockage. If the tube is blocked (e.g., tap is closed), the water will not flow inside the tube.
The same holds true for electric current: the continuous flow of electrons requires there be an unbroken path to permit that flow

## Slide 25: Current to Voltage
The electric charge formed between two materials by rubbing them together serves to store a certain amount of energy (static).
This energy is not unlike the energy stored in a high reservoir of water that has been pumped from a lower-level pond
The influence of gravity on the water in the reservoir creates a force that attempts to move the water down to the lower level again

## Slide 26: Current to Voltage
It takes energy to pump water from the low-level pond to the high-level reservoir, and the movement of water through the piping back down to its original level constitutes a releasing of energy stored from previous pumping (dynamic electricity).
The influence of gravity on the water in the reservoir creates a force that attempts to move the water down to the lower level again

## Slide 27: Current and Voltage
“Pumping” electrons to create an electric charge imbalance results in a certain amount of energy being stored in that imbalance (static).
Just as providing a way for water to flow back down from the heights of the reservoir results in a release of that stored energy, providing a way for electrons to flow back to their original “levels” results in a release of stored energy (dynamic)

## Slide 28: Voltage
When electrons are poised in that static condition (just like water sitting still, high in a reservoir), the energy stored there is called potential energy, because it has the possibility (potential) of release that has not been fully realized yet.
Potential energy, stored in the form of an electric charge imbalance and capable of provoking electrons to flow through a conductor, can be expressed as a term called voltage: a measure of potential energy per unit charge of electrons

## Slide 29: Voltage resembles gravity
An electron at the top of a voltage "hill" travels "downhill" through wires and elements of a circuit. It gives up its potential energy, doing work along the way. When the electron is halfway down the hill, it has given up, or "dropped", half of its potential energy.
For a mass m, a change of height h corresponds to a change in potential energy, ΔU=mgΔh
For a charged particle q, a voltage V corresponds to a change in potential energy, ΔU=qV

## Slide 30: Voltage
Measure of work required to move a unit charge from one location to another, against the force which tries to keep electric charges balanced.
Voltage is the amount of potential energy available (work to be done) per unit charge, to move electrons through a conductor
By Created by User:Omegatron using Klunky schematic editor, which the creator considers public domain (possibly with post-editing in the GIMP or Inkscape) - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=591893
A schematic diagram of a real voltage source, V, driving a resistor, R, and creating a current I

## Slide 31
Incoming radio waves will produce an alternating EM (field shown in green). This EM field will then cause charges to slosh back and forth through the antenna. This oscillating charge in turn will cause the voltage to move up and down (shown in red). Because the geometry was chosen just right, the voltage oscillates like a standing wave.

## Slide 32: Voltage
The potential energy available for moving electrons from one point to another is relative to those two points.
Therefore, voltage is always expressed as a quantity between two points.

## Slide 34: Ohm’s Law: Resistance and Simple Circuits

## Slide 35: What drives current?
We can think of various devices—such as batteries, generators, wall outlets, and so on—which are necessary to maintain a current.
All such devices create a potential difference and are loosely referred to as voltage sources.
When a voltage source is connected to a conductor, it applies a potential difference V that creates an electric field.
The electric field in turn exerts force on charges, causing current.

## Slide 37: Resistance
As electrons work their way through wires, they encounter opposition to motion
This opposition to electric current depends on the type of material, its cross-sectional area, and its temperature.
It is technically known as resistance (R): conductors have low resistance and insulators have very high resistance.
This resistance serves to limit the amount of current through the circuit with a given amount of voltage supplied by the battery

## Slide 38: Resistance
current is cut in half if resistance doubles

## Slide 39: Ohm’s Law
The current that flows through most substances is directly proportional to the voltage V
It can be viewed as a cause-and-effect relationship, with voltage the cause and current the effect.
I α V
The electric property that impedes current (crudely similar to friction and air resistance) is called resistance R
Resistance is defined as inversely proportional to current
I α 1/R

## Slide 40: OHM'S LAW
The law states that the amount of current (I; measured in amperes or amps) flowing in a conductor is related to the potential difference (voltage; V; measured in volts) applied to it.
The constant R (measured in ohms) is resistance of the wire.
I = V/R

## Slide 41: A simple circuit
A closed path for current to flow is supplied by conductors (usually metal wires) connecting a load to the terminals of a battery, represented by the red parallel lines.
The zigzag symbol represents the single resistor and includes any resistance in the connections to the voltage source.
http://cnx.org/contents/031da8d3-b525-429c-80cf-6c8ed997733a@9.94.

## Slide 42
http://cnx.org/contents/031da8d3-b525-429c-80cf-6c8ed997733a@9.94.

## Slide 43: Capacitance
Capacitors introduce a time element into current flow.
They accumulate and store electrical charge and when they are added to a circuit, current and voltage changes are no longer simultaneous.
Consists of two conducting plates separated by an insulator.
When a voltage is applied, there is an instantaneous displacement of charge from one plate to another through the circuit.
Once the capacitor is fully charged, there is no further current as no more current can flow across the insulator.

## Slide 45: RC Circuit: Putting it all together
Time constant, can be calculated: t = RC
  t represents the time constant
  R represents the resistance
  C represents the capacitance

## Slide 46: RC Circuit: Putting it all together
The time constant governs the time it takes to reach a steady state response after a change in the voltage across a membrane.
In both a neuron and an electrical circuit, this voltage rises to the steady state level asymptotically in the response to an external current (e.g., from an action potential). Once the external current is shut off, the voltage drops in a similar asymptotic way
Opening more ion channels (or resistors, as in the RC circuit), which decreases resistance and increases conductance, will express a more rapid increase in voltage on the voltmeter, visually demonstrating the properties of resistance in a neuron.

## Slide 47: Charging a capacitor
When a capacitor (C) is being charged through a resistance (R) to a final potential Vo, the equation giving the voltage (V) across the capacitor at any time t is given by:
V = Vo[1-e-(t/RC)]
As the capacitor charges the charging current decreases since the potential across the resistance decreases as the potential across the capacitor increases.

## Slide 48: Discharge of a capacitor through a resistor
The bigger the value of RC the slower the rate at which the capacitor discharges.
Capacitor discharge (voltage decay):
V = Voe-(t/RC)

## Slide 49
http://neuronsinaction.com/tutorials/membrane

## Slide 50: Points to remember
Dynamic electricity, or electric current, is the uniform motion of electrons through a conductor.
Static electricity is an unmoving (if on an insulator), accumulated charge formed by either an excess or deficiency of electrons in an object. It is typically formed by charge separation by contact and separation of dissimilar materials.
Voltage is the measure of specific potential energy (potential energy per unit charge) between two locations.
  it is the measure of “push” available to motivate electrons.
  Voltage, as an expression of potential energy, is always relative between two locations, or points.

## Slide 51: Points to remember
When a voltage source is connected to a circuit, the voltage will cause a uniform flow of electrons through that circuit called a current.
Resistance is the measure of opposition to electric current.
The capacitor is a component which has the ability or “capacity” to store energy in the form of an electrical charge producing a potential difference (Static Voltage) across its plates, much like a small rechargeable battery.

## Slide 52: Self-assessment
http://philschatz.com/physics-book/contents/m42341.html
http://philschatz.com/physics-book/contents/m42344.html